## Slide 1: Connecticut’s GHG Emissions Inventory
1990-2015

## Slide 2: Goal
Provide an overview of CT’s GHG emissions from 1990-2015, the most recent year for which full data are available.
The statewide GHG emission inventory is an important tool for tracking Connecticut’s progress toward the goals set by PA-08-98.
  Targets of reducing GHG emissions:
  10% below 1990 levels by 2020
  45% below 2001 levels by 2030
  80% below 2001 levels by 2050

## Slide 3: Data/Methods
Heavily based on the U.S. Environmental Protection Agency’s State Inventory Tool (SIT).
  tool calculates sector-by-sector GHG emissions based on numerous state-level data sets
Default data is used most sectors, exceptions are:
  solid-waste data from the DEEP municipal waste program
  LULC and forestry default data not used => unreliable, questionable
  consumption based accounting for the electricity sector based on MA DEP SGIT appendix Q-S methodology
National statistics and state data are used when appropriate from EIA and federal sources
State demographic & transportation data

## Slide 4
Chart: Connecticut Greenhouse Gas Emissions 1990-2015 Comparison of Economy-wide Results Using Two Methods of Accounting for Electricity Sector
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
Total w/ generation-based accounting | 44.6259 | 43.9519 | 44.6305 | 42.9024 | 42.3714 | 42.3416 | 45.7432 | 50.1441 | 47.6939 | 48.9082 | 50.3234 | 49.0491 | 47.3903 | 49.9031 | 51.8286 | 51.0083 | 47.7492 | 46.7461 | 44.3407 | 42.3185 | 42.9364 | 41.6432 | 41.04 | 42.0362 | 42.1111 | 43.363
2020 Goal | 40.1633 | 40.1633 | 40.1633 | 40.1633 | 40.1633 | 40.1633 | 40.1633 | 40.1633 | 40.1633 | 40.1633 | 40.1633 | 40.1633 | 40.1633 | 40.1633 | 40.1633 | 40.1633 | 40.1633 | 40.1633 | 40.1633 | 40.1633 | 40.1633 | 40.1633 | 40.1633 | 40.1633 | 40.1633 | 40.1633
2050 Target | 8.9252 | 8.9252 | 8.9252 | 8.9261 | 8.9261 | 8.9261 | 8.9261 | 8.9261 | 8.9261 | 8.9261 | 8.9261 | 8.9261 | 8.9261 | 8.9261 | 8.9261 | 8.9261 | 8.9261 | 8.9261 | 8.9261 | 8.9261 | 8.9261 | 8.9261 | 8.9261 | 8.9261 | 8.9261 | 8.9261
Total w/ consumption-based accounting | 44.4088 | 44.1919 | 46.1414 | 44.4805 | 44.254 | 42.9249 | 45.1668 | 48.8387 | 47.2945 | 48.9716 | 49.6553 | 49.9763 | 48.9948 | 52.6095 | 53.6381 | 52.0051 | 47.6635 | 47.5696 | 44.9731 | 45.7299 | 45.7 | 43.922 | 41.6982 | 42.7929 | 43.4769 | 44.5085

## Slide 5
Chart: Annual GHG emissions by Sector, 1990-2015
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
Transportation | 15.5954 | 15.5232 | 15.6332 | 15.7266 | 15.6554 | 15.4125 | 16.2062 | 16.2418 | 16.4751 | 17.6876 | 17.1605 | 17.8313 | 17.6743 | 18.1627 | 19.9352 | 18.9585 | 18.0869 | 17.9584 | 16.9546 | 16.435 | 16.1473 | 15.8495 | 15.4311 | 15.4657 | 15.3653 | 15.406
Residential | 8.2682 | 8.0138 | 9.4918 | 9.0692 | 8.6667 | 7.9675 | 8.4507 | 8.1748 | 7.1108 | 8.0297 | 8.7813 | 8.4968 | 8.2309 | 9.7987 | 10.2877 | 9.3488 | 8.0709 | 8.3258 | 8.155 | 8.1954 | 7.651 | 7.2902 | 6.7295 | 7.3375 | 7.5927 | 7.7733
Electric power | 11.9087 | 12.0158 | 11.2827 | 10.2287 | 10.3959 | 10.3204 | 10.7347 | 13.202 | 12.9489 | 12.2101 | 11.9899 | 12.3434 | 11.9837 | 12.3559 | 12.229 | 12.6701 | 11.0814 | 11.2919 | 10.0931 | 11.4542 | 11.965 | 10.4615 | 9.6302 | 9.4731 | 9.8117 | 10.1859
Industrial | 3.2319 | 3.3622 | 3.6199 | 3.7208 | 3.4169 | 3.4043 | 3.6554 | 4.493 | 4.3407 | 4.3725 | 4.6272 | 4.3938 | 4.3713 | 4.7305 | 4.6932 | 4.6146 | 4.5271 | 4.2697 | 3.9295 | 3.9354 | 3.9023 | 4.0393 | 3.9877 | 4.2486 | 4.1956 | 4.0723
Commercial | 3.8299 | 3.6631 | 4.3134 | 3.8473 | 4.1772 | 3.8435 | 4.1361 | 4.3054 | 4.0393 | 4.2952 | 4.5503 | 4.3216 | 4.1316 | 4.96 | 3.942 | 3.751 | 3.326 | 3.3592 | 3.3792 | 3.2951 | 3.3695 | 3.6033 | 3.2592 | 3.5866 | 3.8164 | 4.3367
Waste | 1.2604 | 1.314 | 1.4673 | 1.5414 | 1.5958 | 1.6333 | 1.6877 | 2.1396 | 2.0792 | 2.0684 | 2.2492 | 2.2967 | 2.302 | 2.3162 | 2.2881 | 2.3285 | 2.3121 | 2.0281 | 2.1286 | 2.1089 | 2.3675 | 2.4267 | 2.4045 | 2.4282 | 2.443 | 2.4748
Agricultural | 0.31416 | 0.2998 | 0.33323 | 0.34651 | 0.3461 | 0.34343 | 0.29606 | 0.28219 | 0.30052 | 0.30803 | 0.29696 | 0.29272 | 0.30089 | 0.28557 | 0.26293 | 0.33352 | 0.25912 | 0.33667 | 0.33311 | 0.30589 | 0.29743 | 0.25158 | 0.25599 | 0.25339 | 0.2522 | 0.25939
Generation | 12.1258 | 11.7759 | 9.7718 | 8.6506 | 8.5134 | 9.7371 | 11.3111 | 14.5074 | 13.3482 | 12.1467 | 12.658 | 11.4162 | 10.3792 | 9.6495 | 10.4195 | 11.6733 | 11.1671 | 10.4683 | 9.4607 | 8.0428 | 9.2014 | 8.1827 | 8.972 | 8.7164 | 8.4459 | 9.0405

## Slide 6
Chart: GHG Emissions and Vehicle Miles Traveled
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
Transportation_Emissions | 15.5954 | 15.5232 | 15.6332 | 15.7266 | 15.6554 | 15.4125 | 16.2062 | 16.2418 | 16.4751 | 17.6876 | 17.1605 | 17.8313 | 17.6743 | 18.1627 | 19.9352 | 18.9585 | 18.0869 | 17.9584 | 16.9546 | 16.435 | 16.1473 | 15.8495 | 15.4311 | 15.4657 | 15.3653 | 15.406
Total - w/ Electric Consumption | 44.4088 | 44.1919 | 46.1414 | 44.4805 | 44.254 | 42.9249 | 45.1668 | 48.8387 | 47.2945 | 48.9716 | 49.6553 | 49.9763 | 48.9948 | 52.6095 | 53.6381 | 52.0051 | 47.6635 | 47.5696 | 44.9731 | 45.7299 | 45.7 | 43.922 | 41.6982 | 42.7929 | 43.4769 | 44.5085
VMT | 26306.28 | 26626.02 | 26386.945 | 27017.3821 | 27137.012 | 28044.8283 | 28071.1258 | 28545.6995 | 29179.4655 | 29796.3501 | 30429.9909 | 30760.0012 | 31150.6797 | 31344.1757 | 31476.5021 | 31598.542 | 31723.622 | 31973.4649 | 31564.9368 | 31391.3414 | 31293.5593 | 31197.2468 | 31183.9283 | 30941.1872 | 31190.3154 | 32755.5166

## Slide 7
Chart: GDP and Population
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
GDP (million current $) | 100169 | 101475 | 105759 | 107680 | 113115 | 123212 | 129111 | 140108 | 147911 | 154708 | 169004 | 175290 | 178017 | 183533 | 200407 | 210170 | 221420 | 236640 | 238211 | 233562 | 234528 | 234233 | 239462 | 240975 | 244612 | 253467 | 263379
Population | 3291967 | 3302895 | 3300712 | 3309175 | 3316121 | 3324144 | 3336685 | 3349348 | 3365352 | 3386401 | 3411777 | 3432835 | 3458749 | 3484336 | 3496094 | 3506956 | 3517460 | 3527270 | 3545579 | 3561807 | 3579345 | 3590537 | 3594362 | 3599341 | 3596677 | 3590886 | 3576452
Demographics:
  2015 CT median age = 37.2 yrs
  -7% change in 2015 GHG lbs/capita from 1990
GDP:
  Post-2008 recession, GDP growth has been small (<2% /yr from previous year)
  -60% change in 2015 GHG lbs/GDP from 1990

## Slide 8: Electricity Sector Emissions
CT energy sector electricity consumption & generation were higher than in 2014:
  From EIA: 2015 generation was 7% higher than 2014
  From MA DEP: 2015 consumption was 4% higher
CT also exported MUCH more energy (includes energy used for pumping/storage)
  Many REC imports were from biogenic sources, primarily wood/wood biomass
  Consumed energy sources were also more GHG intensive
Shutdown of the 620-MW Vermont Yankee Nuclear power plant in December 2014?
  For the ISO-NE region, the % of energy supplied from nuclear sources dropped by 4% from 2014 to 2015.
Regional emission factor:
  across the ISO-NE region 2015 was brutally cold, more energy was used & generated.
  Larger percentage of ISO-NE energy mix was from higher emission fuels.
    Regional emission factor was higher than previous year.
Notes: Connecticut’s largest GHG reduction since 1990 has occurred in the electric power sector —14.5% under consumption-based accounting and 25% under generation-based accounting.

## Slide 9
Chart: 2015
| CT | MA | NH | ME | RI | VT
Energy from Generation (GWh) | 32.5 | 31.3 | 18.8 | 8.2 | 7.8 | 1.3
Chart: 2014
| CT | MA | NH | ME | RI | VT
 | 26.2586 | 30.4309 | 18.2868 | 9.178 | 9.8794 | 5.9673
Percent of ISO-NE Energy Generation
 | Net Energy (GWh) |  |  |  |  |  | 
 | Total | ME | NH | VT | CT | RI | MA
Load | 127,176 | 12,045 | 11,702 | 6,009 | 30,961 | 8,204 | 58,254
Generation | 108,357 | 9,945 | 19,815 | 6,466 | 28,453 | 10,705 | 32,974
 | Net Energy (GWh) |  |  |  |  |  | 
 | Total | ME | NH | VT | CT | RI | MA
Load | 126,955 | 11,924 | 11,699 | 5,929 | 31,071 | 8,225 | 58,107
Generation | 107,916 | 8,867 | 20,313 | 1,436 | 35,087 | 8,395 | 33,817

## Slide 10: Biogenic Fuel
Emission Factors from MA DEP methodology | 
 | New England
Non-biogenic GHG Emission Rate (lb/MWh) | 531 (521)
Biogenic GHG Emission Rate (lb/MWh) | 157 (146)
Total | 688 (+3%)
Notes: Emission factors:
Emission factors provide a useful shortcut for use in life-cycle assessment, avoiding the need for detailed calculations of emissions. An emission factor is a typical quantity of GHGs released to the atmosphere per unit of activity (lb/MWh).
The regional (ISO-NE) regional factor is based on the regional mix of fuels. For 2015, the mix had a higher percentage of dirty fuels due to a very cold prolonged winter.

## Slide 11
Chart: 2015 CT RECs
| Biomass | Diesel | Digester Gas | Fuel cell | Hydroelectric/Hydropower | Jet | Landfill gas | Municipal solid waste | Natural gas | Oil | Solar Photovoltaic | Trash-to-energy | Wind | Wood
In CT | 195215 | 468 | 0 | 204112 | 76537 | 121 | 13677 | 326083 | 1003554 | 9552 | 88005 | 404987 | 2154 | 0
From MA | 0 | 0 | 0 | 0 | 9841 | 0 | 47994 | 0 | 0 | 0 | 90 | 5652 | 0 | 113233
to MA | 0 | 0 | 0 | 0 | -24740 | 0 | -4881 | 0 | 0 | 0 | -908 | 0 | 0 | 0
From ME | 3466 | 0 | 0 | 0 | 151773 | 0 | 6401 | 0 | 0 | 0 | 93 | 35576 | 223855 | 1038898
to ME | 0 | 0 | 0 | 0 | -145992 | 0 | 0 | -14723 | 0 | 0 | 0 | -82580 | 0 | 0
From NH | 298471 | 0 | 0 | 0 | 35510 | 0 | 42087 | 0 | 0 | 0 | 436 | 0 | 43327 | 572862
to NH | 0 | 0 | 0 | 0 | 0 | 0 | -1773 | 0 | 0 | 0 | 0 | 0 | 0 | 0
From RI | 0 | 0 | 0 | 0 | 4990 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
to RI | 0 | 0 | 0 | 0 | -582 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
From VT | 290360 | 0 | 3287 | 0 | 133918 | 0 | 25126 | 0 | 0 | 0 | 1265 | 0 | 116370 | 152709
From NY | 0 | 0 | 0 | 0 | 4092 | 0 | 148860 | 0 | 0 | 0 | 0 | 0 | 98303 | 0
From Q | 0 | 0 | 0 | 0 | 25000 | 0 | 19961 | 0 | 0 | 0 | 0 | 0 | 139136 | 0

## Slide 12: Imported Wood Fuel
For 2015, imported wood fuel generated 35,615,057 MMBtu of energy.
  10% reduction => CT biogenic emission factor decreases by 19 (lb/MWh).
  10% reduction => NE regional emission factor decreases by 5 (lb/MWh).
  20% reduction => NE regional emission factor decreases by 11 (lb/MWh).
Notes: For 2015,

## Slide 13
Chart: CT RECs by Source & Year
| 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
Biodiesel1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 138 | 64 | 0 | 0 | 0 | 0
Biomass | 1 | 78448 | 93662 | 102980 | 118551 | 267008 | 381845 | 441590 | 356068 | 356939 | 455653 | 619585 | 787512 | 835611
Diesel | 0 | 0 | 0 | 0 | 0 | 0 | 3158 | 3911 | 1553 | 1024 | 0 | 0 | 468 | 0
Digester Gas | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 343 | 4798 | 9109 | 8656 | 3287 | 7897
Fuel cell | 0 | 2737 | 5966 | 7198 | 7283 | 7939 | 13599 | 12295 | 16590 | 34917 | 59696 | 194101 | 204112 | 258091
Hydroelectric/Hydropower | 91089 | 161520 | 270128 | 344565 | 376902 | 546941 | 504902 | 464985 | 382975 | 257755 | 465199 | 456964 | 441661 | 397545
Jet | 0 | 0 | 0 | 0 | 0 | 0 | 247 | 388 | 248 | 62 | 0 | 0 | 121 | 0
Landfill gas | 29857 | 183428 | 181120 | 127143 | 247760 | 310063 | 367385 | 249633 | 102916 | 166418 | 192383 | 200320 | 304106 | 189534
Municipal solid waste | 751172 | 725182 | 716994 | 708191 | 633518 | 723203 | 206042 | 157637 | 149991 | 265477 | 328339 | 471841 | 326083 | 260311
Natural gas | 0 | 0 | 0 | 0 | 0 | 113353 | 454275 | 569787 | 626649 | 731195 | 804175 | 970505 | 1003554 | 59899
Oil | 0 | 0 | 0 | 0 | 0 | 0 | 53 | 598 | 957 | 1 | 1159 | 5825 | 9552 | 0
Solar Photovoltaic | 0 | 0 | 0 | 0 | 108 | 174 | 3196 | 11605 | 14416 | 17312 | 28718 | 58479 | 89889 | 170214

## Slide 14: New England Winter 2015
2015 was the coldest January-March on record, particularly February
Chart: New England February Normalized Anomalies
| 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
CT_FEB | -2.3 | 7.2 | 1.7 | 3.2 | 8 | 2.8 | -0.6 | 0 | 1.9 | 1.4 | 6.3 | 6.6 | 3.5 | -3.2 | -3.5 | -0.5 | 1.1 | 7.6 | 8.9 | 5.4 | 5 | 3.2 | 7.8 | -2.5 | 2.2 | 3.4 | 3.2 | -3 | 3.5 | 3.9 | 3.5 | 0.8 | 8.7 | 2.9 | -1.3 | -10.5 | 5.7 | 8.3 | 9.3
MA_FEB | -2.2 | 7.3 | 1.1 | 3.3 | 8.3 | 2.9 | -0.4 | -0.4 | 1.8 | 0.8 | 5.1 | 6.6 | 3.2 | -4.2 | -3.1 | -0.5 | 1 | 7.5 | 8.7 | 5.6 | 5.1 | 2.8 | 7.4 | -2.2 | 2.4 | 3.2 | 3.2 | -2.6 | 3.6 | 3.6 | 4.3 | 0.5 | 8.6 | 3.4 | -0.9 | -10.4 | 5.9 | 8.1 | 9.3
ME_FEB | -0.4 | 11.9 | -0.9 | 4.5 | 10.5 | 4.5 | 0.6 | 0.1 | 2.2 | 0.1 | 1.5 | 5.1 | 1.3 | -7.8 | -3.5 | -1.9 | 2 | 3.3 | 9.3 | 6.5 | 3.3 | 1.1 | 5.5 | -2.7 | 3.1 | 4.7 | 4.1 | -3.3 | 3.6 | 4 | 9.7 | 1.3 | 6.5 | 5.1 | 0.8 | -9.7 | 7 | 5.8 | 7.7
NH_FEB | -1.7 | 9.9 | 0 | 4.5 | 9.8 | 3.7 | -0.7 | -0.9 | 1.9 | 0.8 | 3.7 | 6.2 | 3 | -6.5 | -3.7 | -0.8 | 1.1 | 6.4 | 9.3 | 5.9 | 4.3 | 2.3 | 6.5 | -2.2 | 2.2 | 4 | 4 | -3.6 | 3.7 | 3.2 | 6.8 | 0.2 | 8.4 | 4.6 | -0.4 | -10.4 | 7.1 | 8.2 | 8.5
RI_FEB | -2.2 | 6.8 | 1.9 | 3 | 7.8 | 2.4 | -0.4 | -0.3 | 2.3 | 0.5 | 5.1 | 5.8 | 3 | -3.4 | -3.2 | 0 | 0.5 | 7.6 | 8.2 | 5.6 | 5.2 | 3.1 | 7.1 | -2.6 | 3.1 | 2.5 | 2.8 | -2.4 | 4 | 4.2 | 3.6 | 1 | 7.9 | 2.4 | -0.6 | -10.1 | 5.3 | 7.4 | 9.8
VT_FEB | -1.7 | 11.4 | 0.7 | 4.2 | 10.4 | 4 | -1.3 | -2.8 | 1.9 | 0.6 | 4.2 | 6.9 | 2 | -7.3 | -4.1 | -0.8 | 1.9 | 6.7 | 9.6 | 5.7 | 4.3 | 3 | 7.5 | -2.3 | 1 | 4.6 | 4.8 | -3.7 | 4 | 4.1 | 7 | 1.1 | 9.1 | 5 | 0.1 | -11.2 | 7.4 | 9.2 | 9

## Slide 15
Chart: February Anomalies
| 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
CT | -4.756 | 4.7263 | -0.7914 | 0.6909 | 5.4732 | 0.2555 | -3.1622 | -2.5799 | -0.6976 | -1.2153 | 3.667 | 3.9493 | 0.8316 | -5.8861 | -6.2038 | -3.2215 | -1.6392 | 4.8431 | 6.1254 | 2.6077 | 2.19 | 0.3723 | 4.9546 | -5.3631 | -0.6808 | 0.5015 | 0.2838 | -5.9339 | 0.5484 | 0.9307 | 0.513 | -2.2047 | 5.6776 | -0.1401 | -4.3578 | -13.5755 | 2.6068 | 5.1891 | 6.1714
MA | -4.428 | 5.0453 | -1.1814 | 0.9919 | 5.9652 | 0.5385 | -2.7882 | -2.8149 | -0.6416 | -1.6683 | 2.605 | 4.0783 | 0.6516 | -6.7751 | -5.7018 | -3.1285 | -1.6552 | 4.8181 | 5.9914 | 2.8647 | 2.338 | 0.0113 | 4.5846 | -5.0421 | -0.4688 | 0.3045 | 0.2778 | -5.5489 | 0.6244 | 0.5977 | 1.271 | -2.5557 | 5.5176 | 0.2909 | -4.0358 | -13.5625 | 2.7108 | 4.8841 | 6.0574
ME | -2.714 | 9.5652 | -3.2556 | 2.1236 | 8.1028 | 2.082 | -1.8388 | -2.3596 | -0.2804 | -2.4012 | -1.022 | 2.5572 | -1.2636 | -10.3844 | -6.1052 | -4.526 | -0.6468 | 0.6324 | 6.6116 | 3.7908 | 0.57 | -1.6508 | 2.7284 | -5.4924 | 0.2868 | 1.866 | 1.2452 | -6.1756 | 0.7036 | 1.0828 | 6.762 | -1.6588 | 3.5204 | 2.0996 | -2.2212 | -12.742 | 3.9372 | 2.7164 | 4.5956
RI | -4.386 | 4.5891 | -0.3358 | 0.7393 | 5.5144 | 0.0895 | -2.7354 | -2.6603 | -0.0852 | -1.9101 | 2.665 | 3.3401 | 0.5152 | -5.9097 | -5.7346 | -2.5595 | -2.0844 | 4.9907 | 5.5658 | 2.9409 | 2.516 | 0.3911 | 4.3662 | -5.3587 | 0.3164 | -0.3085 | -0.0334 | -5.2583 | 1.1168 | 1.2919 | 0.667 | -1.9579 | 4.9172 | -0.6077 | -3.6326 | -13.1575 | 2.2176 | 4.2927 | 6.6678
VT | -3.903 | 9.1582 | -1.5806 | 1.8806 | 8.0418 | 1.603 | -3.7358 | -5.2746 | -0.6134 | -1.9522 | 1.609 | 4.2702 | -0.6686 | -10.0074 | -6.8462 | -3.585 | -0.9238 | 3.8374 | 6.6986 | 2.7598 | 1.321 | -0.0178 | 4.4434 | -5.3954 | -2.1342 | 1.427 | 1.5882 | -6.9506 | 0.7106 | 0.7718 | 3.633 | -2.3058 | 5.6554 | 1.5166 | -3.4222 | -14.761 | 3.8002 | 5.5614 | 5.3226
NH | -3.964 | 7.6091 | -2.3178 | 2.1553 | 7.4284 | 1.3015 | -3.1254 | -3.3523 | -0.5792 | -1.7061 | 1.167 | 3.6401 | 0.4132 | -9.1137 | -6.3406 | -3.4675 | -1.5944 | 3.6787 | 6.5518 | 3.1249 | 1.498 | -0.5289 | 3.6442 | -5.0827 | -0.7096 | 1.0635 | 1.0366 | -6.5903 | 0.6828 | 0.1559 | 3.729 | -2.8979 | 5.2752 | 1.4483 | -3.5786 | -13.6055 | 3.8676 | 4.9407 | 5.2138

## Slide 16
Chart: Normalized Winter Anomalies and Electric Sector Emissions
| 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
CT_JAN | 2.878 | -7.0128 | -7.0036 | 2.1056 | -2.4852 | -3.276 | 2.2332 | 0.2424 | -2.9484 | 4.6608 | 8.77 | 1.0792 | 2.5884 | 3.4976 | -7.1932 | 6.316 | -0.8748 | 0.7344 | 6.8436 | 1.0528 | -1.838 | -0.7288 | 6.6804 | -5.3104 | -8.1012 | -2.592 | 6.7172 | 4.2264 | 2.5356 | -6.2552 | -0.346 | -4.2368 | 4.1724 | 1.1816 | -4.1092 | -4.5 | 1.8092 | 4.8184 | -2.7724
CT_FEB | -4.756 | 4.7263 | -0.7914 | 0.6909 | 5.4732 | 0.2555 | -3.1622 | -2.5799 | -0.6976 | -1.2153 | 3.667 | 3.9493 | 0.8316 | -5.8861 | -6.2038 | -3.2215 | -1.6392 | 4.8431 | 6.1254 | 2.6077 | 2.19 | 0.3723 | 4.9546 | -5.3631 | -0.6808 | 0.5015 | 0.2838 | -5.9339 | 0.5484 | 0.9307 | 0.513 | -2.2047 | 5.6776 | -0.1401 | -4.3578 | -13.5755 | 2.6068 | 5.1891 | 6.1714
CT_MAR | -1.666 | -0.2862 | -1.5064 | 2.2734 | -5.3468 | 2.633 | 1.0128 | 1.8926 | 0.6724 | -0.3478 | 2.132 | 2.9118 | -2.9084 | -3.4286 | -1.3488 | 2.731 | -3.1892 | -0.8094 | 2.6704 | 0.7502 | 5.23 | -2.5902 | 1.8896 | -0.7306 | 1.2492 | -4.471 | -0.0912 | -1.7114 | -0.3316 | -0.0518 | 6.128 | 0.1078 | 8.8876 | -0.9326 | -6.3528 | -5.973 | 6.2068 | -3.6134 | -0.9336
CT_Consum | 44.4088 | 44.1919 | 46.1414 | 44.4805 | 44.254 | 42.9249 | 45.1668 | 48.8387 | 47.2945 | 48.9716 | 49.6553 | 49.9763 | 48.9948 | 52.6095 | 53.6381 | 52.0051 | 47.6635 | 47.5696 | 44.9731 | 45.7299 | 45.7 | 43.922 | 41.6982 | 42.7929 | 43.477 | 45.2732
CT_Generation | 44.6259 | 43.9519 | 44.6305 | 42.9024 | 42.3714 | 42.3416 | 45.7432 | 50.1441 | 47.6939 | 48.9082 | 50.3234 | 49.0491 | 47.3903 | 49.9031 | 51.8286 | 51.0083 | 47.7492 | 46.7461 | 44.3407 | 42.3185 | 42.9364 | 41.6432 | 41.04 | 42.0362 | 42.1111 | 43.363

## Slide 17: Emissions and climate
Residuals:
Min 1Q Median 3Q Max
-1.47722 -0.34842 0.03994 0.35763 1.35640
Coefficients:
Estimate Std. Error t value Pr(>|t|)
(Intercept) 11.49776 0.14468 79.472 < 2e-16 ***
CT_FEB 0.15197 0.03803 3.996 0.000773 ***
CT_APR -0.17363 0.09758 -1.779 0.091174 .
CT_JUL -0.14843 0.07139 -2.079 0.051379 .
CT_SEP 0.33104 0.09156 3.616 0.001842 **
CT_NOV 0.19299 0.06372 3.029 0.006906 **
CT_DEC -0.06692 0.04076 -1.642 0.117055
---
Signif. codes: 0 ‘***’ 0.001 ‘**’ 0.01 ‘*’ 0.05 ‘.’ 0.1 ‘ ’ 1
Residual standard error: 0.7029 on 19 degrees of freedom
Multiple R-squared: 0.6678, Adjusted R-squared: 0.5629
F-statistic: 6.366 on 6 and 19 DF, p-value: 0.00084

## Slide 18: Looking Forward into 2016, US
Total U.S. emissions decreased from 2015 to 2016 by 1.9%.
The decrease in CO2 emissions from fossil fuel combustion was largely due to:
  large scale substitution from coal to natural gas and other non-fossil energy sources in the electric power sector; and
  warmer winter conditions in 2016 resulting in a decreased demand for heating fuel in the residential and commercial sectors.
    Connecticut=>winter temperatures were 5-6 degrees Fahrenheit above average.

## Slide 19
Chart: CT Electric Sector Emissions
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
Electric Power (Consumption) | 11.9087 | 12.0158 | 11.2827 | 10.2287 | 10.3959 | 10.3204 | 10.7347 | 13.202 | 12.9489 | 12.2101 | 11.9899 | 12.3434 | 11.9837 | 12.3559 | 12.229 | 12.6701 | 11.0814 | 11.2919 | 10.0931 | 11.4542 | 11.965 | 10.4615 | 9.6302 | 9.4731 | 9.8117 | 10.1859 | 9.2892
Electric Power (Generation) | 12.1258 | 11.7759 | 9.7718 | 8.6506 | 8.5134 | 9.7371 | 11.3111 | 14.5074 | 13.3482 | 12.1467 | 12.658 | 11.4162 | 10.3792 | 9.6495 | 10.4195 | 11.6733 | 11.1671 | 10.4683 | 9.4607 | 8.0428 | 9.2014 | 8.1827 | 8.972 | 8.7164 | 7.9571 | 9.0405 | 8.5687

## Slide 20: Electric Sector, New England Emissions